## Slide 1
Uses of Motion
3D shape reconstruction
Segment objects based on motion cues
Recognize events and activities
Image/video enhancement
Track objects
• Correct for camera jitter (stabilization)
• Align images (mosaics)
• Efficient video representations
Video compression (e.g., MPEG2)
Special effects
…
Motion Estimation

## Slide 2
What affects the induced image motion?
Camera motion
Object motion
Scene structure
Motion Estimation

## Slide 3
Even “poor” motion data can evoke a strong percept
Motion Estimation

## Slide 4
Even “poor” motion data can evoke a strong percept
Motion Estimation

## Slide 5: Motion field
The 2D image motion () is a function of:
the 3D motion () and the depth of the 3D point (Z)

## Slide 6: Optical Flow

## Slide 7: Example Flow Fields
Possible ambiguity between zoom and forward translation
Possible ambiguity between sideways translation and rotation
This lesson – estimation of general 2D flow-fields
Next lesson – constrained by global parametric transformations
Is this the FoE (epipole)
or the
optical axis ???

## Slide 8: The Aperture Problem
So how much information is there locally…?
Notes: So what does it mean “motion consistency of small patches”?
Consider for example the following 4 patches.
They all have different patterns of intensities (and seem to have different motions).
Yet, they have been induced by the same global motion.
Therefore, we would like our measure to capture that they are motion consistent.
While these 4 intensity patterns cannot result from the same motion,
therefore we would like our measure to tell us they are inconsistent.
Once again, we want to do than purely based on the intensities of those patches, without estimating their motions.

## Slide 9: The Aperture Problem
Copyright, 1996 © Dale Carnegie & Associates, Inc.
Not enough info in local regions

## Slide 10: The Aperture Problem
Copyright, 1996 © Dale Carnegie & Associates, Inc.
Not enough info in local regions

## Slide 11: The Aperture Problem
Copyright, 1996 © Dale Carnegie & Associates, Inc.

## Slide 12: The Aperture Problem
Copyright, 1996 © Dale Carnegie & Associates, Inc.
Information is propagated from regions with high certainty (e.g., corners) to regions with low certainty.

## Slide 13: Such info propagation can cause optical illusions…
Illusory corners
Notes: So what does it mean “motion consistency of small patches”?
Consider for example the following 4 patches.
They all have different patterns of intensities (and seem to have different motions).
Yet, they have been induced by the same global motion.
Therefore, we would like our measure to capture that they are motion consistent.
While these 4 intensity patterns cannot result from the same motion,
therefore we would like our measure to tell us they are inconsistent.
Once again, we want to do than purely based on the intensities of those patches, without estimating their motions.

## Slide 14: 1. Gradient-based (differential) methods (Horn &Schunk, Lucase & Kanade) 2. Region-based methods (Correlation, SSD, Normalized correlation)
Direct (intensity-based) Methods
Feature-based Methods
(Dense matches)
(Sparse matches)

## Slide 15: Brightness Constancy Assumption
Image J (taken at time t)
Image I (taken at time t+1)

## Slide 16: The Brightness Constancy Constraint
Brightness Constancy Equation:
Linearizing (assuming small (u,v)):

## Slide 17: Observations:
* One equation, 2 unknowns
* A line constraint in (u,v) space.
* Can recover “Normal-Flow” = = (the component of the flow in the gradient direction)
Need additional constraints…

## Slide 18: Horn and Schunk (1981)
Add global smoothness term
Smoothness error
Error in brightness constancy equation
Minimize:
Solve by using calculus of variations

## Slide 19: Horn and Schunk (1981)
Inherent problems:
* Smoothness assumption wrong at motion/depth discontinuities  over-smoothing of the flow field.
* How is Lambda determined…?

## Slide 20: Lucas-Kanade (1981)
Assume a single displacement (u,v) for all pixels within a small window (e.g., 5x5)
Minimize E(u,v):
Geometrically -- Intersection of multiple line constraints
Algebraically -- Solve a set of linear equations

## Slide 21: Lucas-Kanade (1981)
Differentiating w.r.t u and v and equating to 0:
Solve for (u,v) [ Repeat this process for each and every pixel in the image ]
Minimize E(u,v):

## Slide 22: Singularites
Where in the image will this matrix be invertible and where not…?

## Slide 23: Edge
large gradients, all in the same direction
large l1, small l2

## Slide 24: Low texture region
gradients have small magnitude
small l1, small l2

## Slide 25: High textured region
large gradients in multiple directions
large l1, large l2

## Slide 26:  iterate & warp
x
x0
Initial guess:
Estimate:
estimate update
Linearization approximation

## Slide 27: Linearization approximation  iterate & warp
x
x0
estimate update
Initial guess:
Estimate:
+

## Slide 28: Linearization approximation  iterate & warp
x
x0
Initial guess:
Estimate:
Initial guess:
Estimate:
estimate update
+

## Slide 29: Linearization approximation  iterate & warp
x
x0
+

## Slide 30: Revisiting the small motion assumption
Is this motion small enough?
  Probably not—it’s much larger than one pixel (2nd order terms dominate)
  How might we solve this problem?

## Slide 31
==> small u and v ...
u=10 pixels
u=5 pixels
u=2.5 pixels
u=1.25 pixels
image I
image J
iterate
refine
+
Pyramid of image J
Pyramid of image I
image I
image J
Coarse-to-Fine Estimation
Advantages: (i) Larger displacements. (ii) Speedup. (iii) Information from multiple window sizes.

## Slide 32: Optical Flow Results

## Slide 33: Optical Flow Results

## Slide 34: Optical Flow Results
Length of flow vectors inversely proportional to depth Z of the 3D point
Points closer to the camera move faster across the image plane
Images taken from a helicopter flying through a canyon
Computed optical flow [Black & Anandan]

## Slide 35: Lucas-Kanade (1981)
Inherent problems:
* Still smooths motion discontinuities (but unlike Horn & Schunk, does not propagate smoothness across the entire image)
* Local singularities (due to the aperture problem)
Maybe increase the aperture (window) size…?
But no longer a single motion…
 Global parametric motion estimation – next week.

## Slide 36: Motion Estimation Approaches
1. Direct methods
  Directly recover image motion at each pixel from spatio-temporal image brightness variations.
  Dense motion fields, but sensitive to appearance variations.
  Suitable for video and when image motion is small.
2. Feature-based methods (e.g., SIFT + Ransac)
    Extract visual features (corners, textured areas) and track them over multiple frames.
    Sparse motion fields, but more robust tracking.
    Suitable when image motion is large (10s of pixels).

## Slide 37: Motion Magnification
Wu, Rubinstein, Shih, Guttag, Durand, Freeman
“Eulerian Video Magnification for Revealing Subtle Changes in the World”, SIGGRAPH 2012
Result: ..\Course_Intro_2014_2015\baby-iir-r1-0.4-r2-0.05-alpha-10-lambda_c-16-chromAtn-0.1.mp4
Source video: ..\Course_Intro_2014_2015\baby.mp4
Paper + videos can be found on:
http://people.csail.mit.edu/mrub/vidmag

## Slide 38: Motion Magnification
Could compute optical flow and magnify it
But…
very complicated (motions are almost invisible)
Alternatively:
-
- •s

## Slide 39: Motion Magnification
What is equivalent to?
•s
(time)
This is equivalent to keeping the same temporal frequencies, but magnifying their amplitude (increase frequency coefficient).
 Can decide to do this selectively to specific temporal frequencies (e.g., a range of frequencies of expected heart rates).

## Slide 40: Motion Magnification
What is equivalent to?
•s
(time)
- •s
But holds only for small u•s and v•s
Apply to coarse pyramid levels to generate larger motions


## Slide 41
Original
Time-Magnified
Time-Magnified
time
Original
time

## Slide 42: Motion Magnification
Copyright, 1996 © Dale Carnegie & Associates, Inc.
Paper + videos can be found on:
http://people.csail.mit.edu/mrub/vidmag
EVM_NSFSciVis2012.mov

## Slide 43: Motion Magnification
Paper + videos can be found on:
http://people.csail.mit.edu/mrub/vidmag
vidmag.mov

## Slide 44: Annuncements
IDC Computer Vision Day – next Sunday (25/12) (free attendance, but must register) http://cs.haifa.ac.il/hagit/VisionDay/visionDay_2016.html NO LESSON NEXT WEEK!
Deep-Learning Tutorial – next Thursday (29/12) (free attendance, but must register) http://www.wisdom.weizmann.ac.il/~www/pages/dnns_tut/index.html
Computer Vision Winter School - at HUJI (8/1-12/1) (few places left; requires registration) http://www.as.huji.ac.il/cse